Systemd
Agenda
1. Verden før Systemd
2. Diskussionen om Systemd
3. Logging
4. Timers

---
Boot processen
Lidt kerne-kode, hvor der ledes efter et init-program.
 $ cat init/main.c
 [...]
 static noinline int init_post(void)
 {
 [...]
if (execute_command) {
run_init_process(execute_command);
printk(KERN_WARNING "Failed to execute %s. Attempting "
        "defaults...\n", execute_command);
}
run_init_process("/sbin/init");
run_init_process("/etc/init");
run_init_process("/bin/init");
run_init_process("/bin/sh");
panic("No init found. Try passing init= option to kernel.");
}

---
Linux Standard Base Specification (LSB)
- Linux Standard Base Specification (LSB) defines a binary interface for application programs.
- Location: http://refspecs.linux-foundation.org/lsb.shtml
- LSB core-section, chapter 22 defines the so-called "System Initialization".

---
init
202.1
The init process
init is the parent of all processes. It reads the file
/etc/inittab, and creates processes based on it.
A “runlevel” is a software configuration and init can be in one of the following runlevels:
    - Runlevel 0 (reserved): used to halt the system
    - Runlevel 1 (reserved): used to get the system in single user mode
    - Runlevel 2-5: multiuser runlevels
    - Runlevel 6: used to reboot the system
    - Runlevel s or S: Single user mode, /etc/rcS.d/* are executed during boot of the system.
    - Runlevel A, B and C: “on demand” runlevels, the actual runlevel is unchanged, but the actions associated with the level are executed.

---
inittab
Configuring /etc/inittab
- An entry in this file have the format:
id:runlevels:action:process [paramters to process]
A sample inittab:
 id:2:initdefault
 # First script to be executed
 si::sysinit:/etc/init.d/rcS
 l0:0:wait:/etc/init.d/rc 0
 l1:1:wait:/etc/init.d/rc 1
 l2:2:wait:/etc/init.d/rc 2
 l3:3:wait:/etc/init.d/rc 3
 l4:4:wait:/etc/init.d/rc 4
 l5:5:wait:/etc/init.d/rc 5
 l6:6:wait:/etc/init.d/rc 6
 1:2345:respawn:/sbin/getty 38400 tty1
 2:23:respawn:/sbin/getty 38400 tty2

---
rc
/etc/init.d/rc
For each of the runlevels 0-6 there is an entry in:
/etc/inittab that executes:
/etc/init.d/rc ?
So /etc/init.d/rc is called with the runlevel as a parameter
The rc-script now inspect the corresponding directory for processes to stop and start.
  l2:2:wait:/etc/init.d/rc 2

---
init.d
/etc/rc directories
The directory /etc contains several, runlevel specific, directories:
Each of these contain runlevel specific links to scripts in
/etc/init.d:
    - K* Scripts are executed with “stop” as argument
    - S* scripts are executed with “start” as argument
    - The K* and S* scripts are named with a 2 digit number followed by a name in order to control the order of execution (eg. K20gpm).
$ ls -d /etc/rc.d/rc*
/etc/rc.d/rc0.d /etc/rc.d/rc3.d /etc/rc.d/rc6.d
/etc/rc.d/rc1.d /etc/rc.d/rc4.d /etc/rc.d/rcS.d
/etc/rc.d/rc2.d /etc/rc.d/rc5.d

---
chkconfig and update-rc.d
It is not recommended to manual create or remove links from /etc/init.d/ to the right runlevel under /etc/rc.d/
Instead one of the commands chkconfig or update-rc.d depending on the distribution.
- chkconfig:	suse, redhat, centos, fedora, ...
- update-rc.d:	ubuntu, debian, linux mint, ...